## Slide 1: On Recovering IP Information from EM Data
Doug Oldenburg*, Dave Marchant, Dikun Yang, Seogi Kang, and Eldad Haber

## Slide 2: Outline
Background for IP problem
Forward problem in the time domain
Inverse problem
Field example Mt. Milligan
Conclusions and the path ahead

## Slide 3: Electrical conductivity is complex
Cole-Cole model
Conductivity often represented as
Cole-Cole model but that is not crucial
ω=0
ω=∞

## Slide 4: Different experiments
J
J
J pol
I
V
Current
Voltage

## Slide 5: Inverse problem: two paths
1. Directly in time domain
2. Linearized inversion

## Slide 6: Complex conductivity
σ∞ is background conductivity
Obtained from early times that are not contaminated with IP effects.
The IP effect is a perturbation. This is a good approximation when η is small and has been traditionally used

## Slide 7: IP data and EM coupling removal
Routh and Oldenburg (2001)
Conductivity
Linearization
Removing EM coupling
Background conductivity

## Slide 8: Need background conductivity (σ∞)
Carry out 3D inversion of the AEM data (leave out time channels that have negative transients)
Methodology: Yang and Oldenburg [AGU, 2012, ASEG 2012]
Local mesh for forward modelling and sensitivities
Stochastic selection of transmitters

## Slide 9: Synthetic example
True model
Discretization
  - 20 m core cells
  - 69 x 69 x 50 cells
Background
  σhalf = 5e-4 S/m
Target
  - σ∞ =6.25e-2 S/m
  - η = 0.2
  - τ = 0.01
  - 80m x 80m x 80m
  - 60m below surface
Depth (m)
-60
-160
East-West (m)
-400
-30
50
400
800 m
800 m
East-West
North-South

## Slide 10: Synthetic example
Geometry
VMD source
  30m above surface
  Collocated Rx
7×31 = 217 Txs
Receivers
  - Collocated with Tx
  - Measuring db/dt
  14 time channels
  10-3 – 10-1 seconds

## Slide 11: Synthetic Airborne EM data
At x = 0 m (EW) and y = 0 m (NS)
Notes: It seems that something wrong need to ask dikun?

## Slide 12: Synthetic Airborne EM data
db/dt data at time = 0.003s
log10 (db/dt)
log10 (db/dt)
db/dt (T/s)
Notes: It seems that something wrong need to ask dikun?

## Slide 13: Synthetic Airborne EM data
db/dt data at time = 0.006s
log10 (db/dt)
log10 (db/dt)
db/dt (T/s)
Notes: It seems that something wrong need to ask dikun?

## Slide 14: Synthetic Airborne EM data
db/dt data at time = 0.012s
log10 (db/dt)
log10 (db/dt)
db/dt (T/s)
Notes: It seems that something wrong need to ask dikun?

## Slide 15: Synthetic Airborne EM data
db/dt data at time = 0.024s
log10 (db/dt)
log10 (db/dt)
db/dt (T/s)
Notes: It seems that something wrong need to ask dikun?

## Slide 16: Linear Inversion
At each time
3D volume of

## Slide 17: Recovered pseudo chargeability
Depth (m)
-60
-160
East (m)
-400
-30
50
400
Without depth weighting
With depth weighting
<Cross section>
Sensitivity volume
Depth weighting

## Slide 18: Recovered pseudo chargeability
At four different time channels
Depth (m)
-60
-160
East (m)
-400
-30
50
400
t1 = 0.02s
t3 = 0.024s
t2 = 0.05s
t4 = 0.1s

## Slide 19: Effects of background conductivity
True
background (σ∞)
Wrong
Background (2×σ∞)
Wrong
background (0.5×σ∞)
Notes: It seems that something wrong need to ask dikun?

## Slide 20: Procedure
Compute dIP data at multiple time channels
Subtract regional to obtain
IP data
Invert individual
time channels
Invert TEM to recover a background 3D σ model
Attempt to avoid soundings/times that have IP coupling effects
Easy if there are negative transients
Estimate a regional field
Assume IP data are composed of a smoothly varying regional plus true IP data
Not easy; but this issue is confronted before

## Slide 21: Field example: Mt. Milligan VTEM
Geotech (2007)
Recovered 3D conductivity model
Observed data (db/dt)
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 22: Mt. Milligan Airborne EM data
db/dt data at time = 0.00463s
Observed
Predicted
dIP
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 23: Mt. Milligan Airborne EM data
db/dt data at time = 0.00473s
Observed
Predicted
dIP
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 24: Mt. Milligan Airborne EM data
db/dt data at time = 0.00488s
Observed
Predicted
dIP
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 25: Mt. Milligan Airborne EM data
db/dt data at time = 0.00508s
Observed
Predicted
dIP
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 26: Mt. Milligan Airborne EM data
db/dt data at time = 0.00537s
Observed
Predicted
dIP
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 27: Mt. Milligan Airborne EM data
db/dt data at time = 0.00577s
Observed
Predicted
dIP
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 28: Mt. Milligan Airborne EM data
db/dt data at time = 0.00635s
Observed
Predicted
dIP
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 29: Mt. Milligan Airborne EM data
db/dt data at time = 0.00715s
Observed
Predicted
dIP
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 30: Observed data for all channels
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 31: dIP data for all channels
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 32
Removal of a regional
dIP
regional
data for inversion

## Slide 33
Inversion Results
Depth=20m
Depth=60m
Depth=40m

## Slide 34: Summary and path forward
Estimating σ∞ , 3D background conductivity. (be mindful of IP coupling)
dIP = dobs – F[σ∞ ]
For each time channel:
  Assume: dIP = dIP(true) + smooth background signal
Estimate background signal (challenge)
Individual inversions and then attempt to extract spectral information

## Slide 35: Summary and path forward
More advanced inversions to work with all time channels at once.
Current progress provides optimism that we can invert the data if it is sufficiently high quality

## Slide 36
Acknowledgements
This work was carried out under NSERC CRD and IRC programs and sponsoring companies: Cameco, Teck, Newmont, Barrick, Vale, Xstrata Nickel and Anglo American.
The authors thank Roman Shekhtman for his assistance in programming.
Dikun Yang, Seogi Kang, Dave Marchant
Slide 36 / 31
AEM 2013

## Slide 37: Recovered pseudo chargeability
At four different time channels
Depth (m)
-60
-160
East (m)
-400
-30
50
400
t1 = 0.02s
t3 = 0.024s
t2 = 0.05s
t4 = 0.1s
Take one pixel and plot pseudo chargeability
( ) as a function of time

## Slide 38: Results at a single pixel
Pseudo chargeability ( ) vs. time
Yuval and Oldenburg (1997)
Fitting estimated ( )
Division | Estimated | True
a | -4.0 | 25
b | -70.7 | -125
Notes: Maybe a slide with a few Frequency domain conductivities and the representative sigma(t)
Equations written in convolution format

## Slide 39: Background
Maxwell’s equations in time
Ohm’s law in frequency domain
Ohm’s law in time domain
σ (ω)
σ (t)
Notes: From abstract and elsewhere

## Slide 40: Forward modelling: time domain
Auxiliary equations approach
Cole-Cole model, c = 1
Notes: Maybe a slide with a few Frequency domain conductivities and the representative sigma(t)
Equations written in convolution format

## Slide 41: Numerical experiments
Current density section with IP body

## Slide 42: Numerical experiments
Measured magnetic field (hz)
Rx
IP responses
Rx