## Slide 1: On Recovering IP Information from airborne time domain EM Data
Seogi Kang*, Doug Oldenburg, David Marchant, and Dikun Yang

## Slide 2: Induced polarization
Exploration of massive sulphide deposits
(Mining application)
IP responses in Airborne
Time domain EM (ATEM)
Field example: Mt. Milligan data
VTEM
Coincident loop
Measure dbz/dt

## Slide 3: Field example: Mt. Milligan VTEM
Recovered 3D conductivity model
Yang et al., 2012
Geotech (2007)
Observed data (db/dt)
Negative transients of db/dt
Existence of IP body
(Weidelt, 1982)
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 4: Observed data for all channels
We can “measure” negative transients in the field data (VTEM)
, but only can identify in “late time” channels
Notes: Need to change Figures: Rerun forward modeling based on more sources?
- Need to play with interpolation

## Slide 5: Outline
Backgrounds
Build up conceptual model and verify
Suggest some ways to process and invert IP responses in VTEM data
Conclusions and the path ahead

## Slide 6: Conductivity is frequency dependent
ω=0
ω=∞
Cole-Cole model
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 7: Conductivity is time dependent
σ∞δ (t)
∆σ(t)
Assuming Cole-Cole model for c = 1
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Intrinsic pseudo-chargeability

## Slide 8: Background
Maxwell’s equations in time
Ohm’s law in frequency domain
Ohm’s law in time domain
σ (ω)
σ (t)
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: From abstract and elsewhere

## Slide 9: Convolution approach
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: Modify Ja as Jip

## Slide 10: Convolution approach
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
JIP has opposite direction to JF
Magnitude of JIP is proportional to pseudo chargeability

## Slide 11: Conceptual model
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
JIP has opposite direction to JF
Magnitude of JIP is proportional to pseudo chargeability

## Slide 12: Linearization in EIP or MIP
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 13: Extension to time domain EM
This is our goal:
Decomposition of EM responses

## Slide 14: Our strategy
First linearize JIP
Then use Biot-Savart Law

## Slide 15: Details

## Slide 16: Forward modelling: time domain
Auxiliary equations approach
Cole-Cole model, c = 1
Marchant et al. (2014)
A tool to compute Airborne TEM-IP responses
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: Maybe a slide with a few Frequency domain conductivities and the representative sigma(t)
Equations written in convolution format

## Slide 17: Synthetic example
Conductivity model
Discretization
  - 20 m core cells
  - 69 x 69 x 50 cells
Background
  σhalf = 5e-4 S/m
Target
  - σ∞ = 5e-4 S/m
  - η = 0.2
  - τ = 0.01
  - 80m x 80m x 80m
  - 60m below surface
Depth (m)
-60
-160
-400
400
800 m
800 m
East-West
North-South
East-West (m)
-30
50
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 18: Synthetic example
IP model
Discretization
  - 20 m core cells
  - 69 x 69 x 50 cells
Background
  σhalf = 5e-4 S/m
Target
  - σ∞ = 5e-4 S/m
  - η = 0.2
  - τ = 0.01
  - 80m x 80m x 80m
  - 60m below surface
Depth (m)
-60
-160
East-West (m)
-400
-30
50
400
800 m
800 m
East-West
North-South
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 19: Synthetic example
Geometry
VMD source
  - 30m above surface
  - Coincident loop
  - Step-off waveform
7×14 = 112 Tx-Rx pair
Receivers
  - Collocated with Tx
  - Measuring db/dt
  - 10-5 – 10-1 seconds
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 20: ATEM-IP case: Conceptual model
J IP
J IP
I (current)
J EM
J IP
JEMIP = JEM+JIP
EMIP: with IP effect
EM: without IP effect
y
x
z
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: It seems that something wrong need to ask dikun?

## Slide 21: ATEM case without IP effect (EM)
Total current density (Jtotal) section
J EM
y
x
z
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: It seems that something wrong need to ask dikun?

## Slide 22: ATEM case with IP effect (EMIP)
Total current density (Jtotal) section
I (current)
J IP
J EM
y
x
z
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: It seems that something wrong need to ask dikun?

## Slide 23: ATEM IP effect
Plan view
I (current)
I (current)
J EM
Jtotal without IP
Jtotal with IP
J IP
J EM
JEMIP = JEM+JIP
East
North
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: It seems that something wrong need to ask dikun?

## Slide 24: ATEM IP effect
Plan view
Jtotal without IP
Jtotal with IP
J IP
J EM
Compatible with conceptual model
More chances to observe IP response in late times
J EM
East
North
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: It seems that something wrong need to ask dikun?

## Slide 25: Measured ATEM responses
db/dt response at (0, 0)
EMIP: with IP effect
EM: without IP effect
EMIP = F[σ∞+∆σ(t)]
EM = F [σ∞]
dIP = F [σ∞+∆σ(t)]- F [σ∞]
EM decoupling process
ATEM responses
σ (t) = σ∞δ (t) +∆σ (t)
F[σ∞δ (t) +∆σ (t)]
F[σ∞δ (t)]
dIP
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: It seems that something wrong need to ask dikun?

## Slide 26: Synthetic Airborne EM data
db/dt data at time = 0.0029s
db/dt (T/s)
db/dt (T/s)
db/dt (T/s)
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: It seems that something wrong need to ask dikun?

## Slide 27: Synthetic Airborne EM data
db/dt data at time = 0.012s
db/dt (T/s)
db/dt (T/s)
db/dt (T/s)
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: It seems that something wrong need to ask dikun?

## Slide 28: Synthetic Airborne EM data
db/dt data at time = 0.049s
db/dt (T/s)
db/dt (T/s)
db/dt (T/s)
Accurate estimation of background model (σ∞) is crucial
F[σ∞δ (t) +∆σ (t)]
F[σ∞δ (t)]
dIP
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: It seems that something wrong need to ask dikun?

## Slide 29: Need background conductivity (σ∞)
Carry out 3D inversion of the AEM data (leave out time channels that have negative transients)
Methodology: Yang and Oldenburg [AGU, 2012, ASEG 2012]
Local mesh for forward modelling and sensitivities
Stochastic selection of transmitters
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 30: Linearization of EMIP responses
Linearization
Cole-Cole model (c = 1)
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Pseudo chargeability

## Slide 31: Linear Inversion
At each time
3D volume of
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 32: Recovered pseudo chargeability
Estimated
For three different time channels
Depth (m)
-60
-160
East (m)
-400
-30
50
400
Pseudo chargeability
t = 1.2 ms
t = 2.4 ms
t = 10 ms
Pseudo chargeability c=1
True
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 33: Procedure for ATEM-IP inversion
Compute dIP data at multiple time channels
Subtract regional to obtain
IP data
Invert individual
time channels
Invert TEM to recover a background 3D σ model
Attempt to avoid soundings/times that have IP coupling effects
Easy if there are negative transients
Estimate a regional field
Assume IP data are composed of a smoothly varying regional plus true IP data
Not easy; but this issue is confronted before
??
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 34: Mt. Milligan Airborne EM data
db/dt data at time = 0.00463s
Observed
Predicted
dIP
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 35: Mt. Milligan Airborne EM data
db/dt data at time = 0.00473s
Observed
Predicted
dIP
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 36: Mt. Milligan Airborne EM data
db/dt data at time = 0.00488s
Observed
Predicted
dIP
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 37: Mt. Milligan Airborne EM data
db/dt data at time = 0.00508s
Observed
Predicted
dIP
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 38: Mt. Milligan Airborne EM data
db/dt data at time = 0.00537s
Observed
Predicted
dIP
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 39: Mt. Milligan Airborne EM data
db/dt data at time = 0.00577s
Observed
Predicted
dIP
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 40: Mt. Milligan Airborne EM data
db/dt data at time = 0.00635s
Observed
Predicted
dIP
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 41: Mt. Milligan Airborne EM data
db/dt data at time = 0.00715s
Observed
Predicted
dIP
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 42: Observed data for all channels
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 43: dIP data for all channels
Observed
Predicted
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data
We can better identify dIP through this processing
Notes: From the data we observe the effects of the large negative but there are also other minima.
Unfortunately there seems to be systematic biases and we’ve attempted to remove these with the idea that the broad background should be non-chargeable. This is akin to removing a regional and there is the possibiity of throwing the baby out with the bathwater.
Persevere to get …

## Slide 44
Removal of a regional
dIP
regional
data for inversion
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 45
Inversion Results
Depth=20m
Depth=60m
Depth=40m
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 46: Summary and path forward
We can measure negative transients, which may indicate existence of IP body with VTEM
Build up conceptual model based on Seigel (1959)
and verified with numerical experiments
  Use EMTDIP code developed by Marchant et al., 2012
Better identify IP responses in ATEM-IP data
EMIP or observed
EM or predicted from TEM inversion

## Slide 47: Summary and path forward
Estimate σ∞ , 3D background conductivity
  Use efficient 3D ATEM inversion algorithm developed by Yang and Oldenburg (2012)
Recovered 3D distribution of pseudo chargeability
Current progress provides optimism that we can invert the data if it is sufficiently high quality

## Slide 48: Thank you 

## Slide 49: Effects of background conductivity
True
background (σ∞)
Wrong
Background (2×σ∞)
Wrong
background (0.5×σ∞)
Notes: It seems that something wrong need to ask dikun?

## Slide 51
Acknowledgements
This work was carried out under NSERC CRD and IRC programs and sponsoring companies: Cameco, Teck, Newmont, Barrick, Vale, Xstrata Nickel and Anglo American.
The authors thank Roman Shekhtman for his assistance in programming.
Dikun Yang, Dave Marchant

## Slide 53
m
×10
10-1
10-3
10-1.2
10-1.4
10-1.6
10-1.8
10-2.0
10-2.2
10-2.4
10-2.6
10-2.8
Conductivity (S/m)
dhz/dt (A/m-s)
Comparison between dIP and σ
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 54
Where are IP bodies?
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 55
Where are IP bodies?
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 56
Where are IP bodies?
Hard to identify even from dIP responses
Need to apply inversion technique
Anomalous dIP
Anomalous σ
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data

## Slide 57: How do we do geophysics?
1. Identification of anomalous responses in the data
Good 
3. Extract information of the subsurface as much as we can
  Processing
  Geophysical inversion
2. Try to rationalize these responses based on physics
Negative transients of db/dt
Need to build up conceptual model
How to better identify IP responses?
How to invert these responses?
Lots of things to do 

## Slide 58: Recovered pseudo chargeability
Time decaying at one pixel
Depth (m)
-60
-160
East (m)
-400
-30
50
400
Pseudo chargeability
Pseudo chargeability c=1
We solve this … for
Backgrounds
Conceptual model
dIP responses
Linear inversion
Mt. Milligan data